## Slide 1
🏭 INDUSTRIAL MAINTENANCE COPILOT
The Factory Floor
A safety-first diagnostic agent for electric motors and variable-frequency drives
AI Engineering Bootcamp — Final Project · Retrieval, Agents, Vision, Safety, Evaluation

## Slide 2
01 · THE PROBLEM
Diagnosing a fault means digging through hundreds of pages, fast
Manuals are huge, not searchable
One VFD family alone spans 6 documents and thousands of pages of operating, list, and function manuals — no full-text search on the shop floor.
Machine history lives elsewhere
Past faults and repairs for a specific asset are rarely connected to the manual an operator is reading right now.
Wrong guidance is a safety risk
A confident but ungrounded answer isn't just unhelpful in this domain — skipping a precaution before opening a live drive is dangerous.
The Factory Floor — Industrial Maintenance Copilot
2

## Slide 3
02 · WHAT WE BUILT
One copilot, four components working together — not four separate demos
🔍
RAG
Grounded answers, cited by file + page, from 11 real Siemens manuals — never invents a fault code.
🤖
Agent
Decides which tools to use — manuals, machine history, or neither — and carries memory across turns.
📷
Vision
Classifies visible defects in an uploaded photo — trained classifier, benchmarked against two baselines.
🛡️
Safety
Every physically-performed step is preceded by safety precautions — audited, not just promised.
The Factory Floor — Industrial Maintenance Copilot
3

## Slide 4
03 · ARCHITECTURE
A model that chooses its own tools — not a fixed pipeline
OPERATOR
Question + photo
DIAGNOSTIC AGENT
Decides which tools
search_manuals
RAG · 11 manuals
get_maintenance_history
Past faults for this asset
SAFETY-FIRST RULE
Precautions before action
VISION (optional)
Photo → condition
FINAL ANSWER
Root cause + citations
Both tools are optional — a general question offers only search_manuals. Vision runs before the agent reasons, as context, not a tool it chooses.
The Factory Floor — Industrial Maintenance Copilot
4

## Slide 5
04 · THE DATA
Real manufacturer documentation, not synthetic text
11
manuals
official Siemens PDFs
3,679
pages ingested
chunked + embedded
~3:1
VFD : motor pages
down from 18:1 in the first draft
20
simulated assets
10 motors + 10 VFDs, real fault codes
SINAMICS G120 / G120C (VFD) + SIMOTICS SD / GP (electric motor) — operating instructions, list manuals, function manuals, an engineering manual, and a catalog.
17 real VFD fault codes (e.g. F30021 ground fault, F30059 internal fan fault) extracted by scanning the raw PDF text for the real F/A-code pattern — not guessed from generic Siemens convention. Electric motors genuinely have no numeric fault-code system; confirmed by the same scan returning zero matches.
The Factory Floor — Industrial Maintenance Copilot
5

## Slide 6
05 · RAG + AGENT
Grounded retrieval, combined with real decision-making
Retrieval-Augmented Generation
Every answer is grounded in the actual retrieved manual text, cited by file name + page number — never a source number that could go stale across calls.
"F30059 internal fan fault" →
Siemens SINAMICS G120C List Manual, page 214
Conversation memory
A follow-up like "what if it clears before I check?" is understood in context — the system carries the conversation, not just the last question.
Real decision-making, not a script
"F30021, ground fault checks" (VFD-06 selected)
→ calls search_manuals + get_maintenance_history, cites 2022-06-25 history
Photo (structural damage) + "just a tiny cosmetic scuff"
→ 0 tools called — asks a clarifying question instead of guessing
"What is a VFD?"
→ answers directly, no tools, no fabricated citation
The Factory Floor — Industrial Maintenance Copilot
6

## Slide 7
06 · VISION
A trained classifier, benchmarked honestly against two baselines
82.2%
Trained classifier
frozen ResNet18 features + LogisticRegression
77.1%
Majority-class baseline
always predicting "good"
42.5%
Zero-shot LLM baseline
worse than the trivial baseline
Curated 4-category subset of MVTec AD (cable, metal_nut, screw, transistor) — physically plausible on/around motors and VFDs, 1,502 images. The zero-shot model actually scores below simply guessing "good" every time — a real, honestly-reported failure, not tuned away.
The Factory Floor — Industrial Maintenance Copilot
7

## Slide 8
07 · SAFETY-FIRST BY DESIGN
Measured, not assumed — the same question, with and without the rule
40.0%
Agent — rule 6 active
12 of 30 answers still ordered precautions wrong
94.1%
Baseline — no safety rule
32 of 34 answers put precautions after the steps, or omitted them
A dedicated LLM judge cross-checked by a deterministic keyword rule (91.9% / 78.4% agreement) audits every answer that recommends a physical action. The rule substantially reduces failures — it does not eliminate them, and that's reported as-is, including a live UI ordering failure caught during testing.
The Factory Floor — Industrial Maintenance Copilot
8

## Slide 9
08 · EVALUATION
37 real troubleshooting scenarios, agent vs. baseline, identically scored
78.4%
Root cause — agent
vs. 75.7% baseline
45.9%
Evidence — agent
vs. 48.6% baseline
0%
Baseline history score
structural — no history tool at all
37
scenarios (≥30 req.)
verified against the real corpus
Honest finding worth repeating in the room
On the held-out conflicting-signals case (structural damage photo + "just a cosmetic scuff" text), the agent asked a clarifying question. The baseline — with no vision-context mechanism — took the text at face value and concluded it was "likely safe to continue running the drive."
Evidence accuracy is close between the two — an honest echo of a real, documented limitation: embedding retrieval alone is unreliable for exact fault codes without extra machinery this project doesn't have yet.
The Factory Floor — Industrial Maintenance Copilot
9

## Slide 10
09 · REPORTED HONESTLY
What's real about this system's limits, and what's next
Known limits, not hidden
Embedding search struggles with exact alphanumeric fault codes without a paired symptom.
No relevance threshold yet — an off-topic question still populates a sources table.
Vision dataset is a curated academic benchmark (MVTec AD), not real motor/VFD failure photos.
Safety Validator is an audit utility today, not yet a live blocking gate in the app.
What's next
Hybrid (lexical + semantic) retrieval for exact fault codes.
Real motor/VFD component photos to replace the generic MVTec subset.
A live-blocking version of the Safety Validator inside the app itself.
A Safety Data Sheet corpus, for product-specific (not just equipment-general) precautions.
The Factory Floor — Industrial Maintenance Copilot
10

## Slide 11
ALL 7 BOOTCAMP CORE REQUIREMENTS — ✅ DONE
Now, live.
A real question, a real photo, running against the deployed app — not slides.
The Factory Floor — Industrial Maintenance Copilot · Thank you